## Slide 1
Capewell Solid-State Timer
Team 9:
ME: Patrick Dunham and Joshua Reinhart
EE: Patrick Meres, Robert Endrizzi, Nicole Hershman, and Jaileen Algarin
Faculty Advisors: Dr. Rajeev Bansal & Dr. Thanh Nguyen
Sponsor Representative: Andrew Smith
Notes: Patrick

## Slide 2: Presentation Outline
Project Requirements
Current Standing
  Microcontroller (MCU)
  Relays
  Power Supply
  User Interface (UI)
  Mounting Platform
Schedule
Moving Forward
Notes: Josh

## Slide 3: Project Requirements
Redesign C10B Electromechanical Cycle Timer
  Match current timer in size and function
  Completely solid-state design
Deliverables: Solid-State Timer Design & Source Code
  PCB Design/Schematic
  Mounting platform CAD Files
  Microcontroller Source Code
  Working Prototype
Solid-State Timer PCB
Cams
Motor
Switches
8-Cam C10 Cycle Timer
3.3”
5.6”
2.72”
About Capewell
Notes: Josh

## Slide 4: Microcontroller: Schematic
Relay Controller (x8)
USB Connector
Microcontroller
Notes: Patrick

## Slide 5: Microcontroller: Board Design
Current Prototype
2.5”
2.0”
Notes: Patrick

## Slide 6: Microcontroller: Board Design
Current Prototype
2.5”
2.0”
Power
USB
Programming
Microcontroller
Notes: Patrick

## Slide 7: Solid-State Relays: Schematic
Optoisolator
TRIAC
Load
Notes: Josh
Optoisolator protects circuit from high voltage (120 V from wall)
TRIAC turns on and off high loads, snubber circuit makes sure TRIAC turns off
Load connector used to connect to whatever we’re powering
Essentially, this is an electrically controlled SPST (Single Pole, Single Throw or Closed/Open) switch

## Slide 8: Solid-State Relays: Board Design
Notes: Josh
This is the PCB – next slide!!

## Slide 9: Solid-State Relays: Board Design
Optoisolator
TRIAC
Load
Notes: Josh
This PCB is laid out in the same order as the schematic. Optoisolator to the left, TRIAC near the middle, Load connector to the right
The big red things are PCB copper pours. The left one is a ground plane, the right ones (there’s a blue one under the red one) are to handle high load current

## Slide 10: Solid-State Relays: Assembled Board
Optoisolator
TRIAC
Load
Notes: Josh
Here’s some assembled boards

## Slide 11: Solid-State Relays: Simulation Data
Roughly 1 Watt of power must be dissipated per Ampere of current through each relay
Notes: Josh
Here’s simulation data collected on TRIAC power dissipation versus load current. The trend is roughly linear, and depends very little on power factor
This matches the datasheet!
(side note, the TRIACS are more than 99% efficient)

## Slide 12
At 15 A, 15 W of heat is produced
Ambient Temp = 60 C
Max Device Temp = 150 C
Need heatsink w/ RTH< 3.13 K/W
Solid-State Relays: Heat Sinks
Reduce relays to 10 A rating
Smaller heat sinks fit closer together
Heat sinks too big for allotted space
Heat sinks fit with staggered relay redesign
5.6”
2.72”
Notes: Josh
Figure taken from BT139-800E data sheet

## Slide 13: Power Stage: Board Mount Solution
AC/DC Converter
Cost: ~$12
Output Voltage: 5 V
Output Current: .6 A
Power: 3 W
Input Voltage: 85-264 VAC
Power Converter Chip
0.9”
1.5”
Notes: Patrick

## Slide 14: Power Stage: Custom Solution
Multistage Switching Converter: Primary Flyback Converter Schematic
Controller
Rectifier
Flyback Converter
Flyback Converter Basics
Notes: Patrick

## Slide 15: Buck Converter Schematic
Multistage Switching Converter: Secondary Buck Converter Schematic
Controller/Converter
Buck Converter Basics
Notes: Patrick

## Slide 16: User Interface (UI)
Graphic Display
Graphic LCD Screen
  128x64 pixel display
  Operates in up to 70° C conditions
  Interfaces w/ Microcontroller
User control: Capacitive Buttons
  Durability, cost, easy, smaller chance of false readings
2.953”
2.075”
Capacitive Buttons
Notes: Patrick

## Slide 17: UI: Design
Display for LCD Screen
Button Layout
Timing Diagram
Each Pixel Represents .25 seconds
Notes: Patrick

## Slide 18: Mounting Platform: Operation
Must match original enclosure footprint
Extruded aluminum
Does not need to be dustproof or waterproof
  Concerns are responsibility of customer
Notes: Josh

## Slide 19: Mounting Platform: Design
Dimensions in inches
Notes: Josh

## Slide 20: Schedule
Mar. 2 – Custom Power Supply Prototyping Begins
Mar. 5 – Finish and Test UI Coding
Mar. 5 – Testing Relay Operation (Controlled by MCU) With Toaster Oven
Mar. 5 – Redesign All Boards for SMD
Mar. 17 – Test Shrunken Boards and Redesign as Single PCB
Mar. 31 – Test Single PCB. (Redesign if Necessary)
(Apr. 14 – Test Redesigned Single PCB in Necessary)
Notes: Patrick

## Slide 21: Moving Forward
Finish Coding UI
Redesign Component PCBs for SMD, then Integrate
3D Print New Mounting Platform Design
Assemble overall prototype using PCB and Mounting Platform
GOTO: 2
Notes: Patrick

## Slide 22: Risk Cube
UI Coding Doesn’t Work
Larger Heat Sinks Fail Original Requirements
Shipping Delays
PCB Mistakes
1
2
3
4
Notes: Josh

## Slide 23: Risk Assessment
UI Coding Doesn’t Work
- UI requires computer & USB connection
Larger Heat Sinks Fail Original Requirements
- De-rate TRIACs to 10A
Shipping Delays
- Rush items, spend more money
PCB Mistakes
- Rush items, spend more money
- No time for more than 2 revisions
Notes: Josh

## Slide 24: Estimated Unit Cost
Item | Cost
MCU | $6
8 Relays | $9
Power Converter | $11
LCD | $10
PCB + Mounting Platform | $5
Total | $41
Estimated cost does not include labor
Notes: Josh

## Slide 25: Team Assessment
Presentation Style
Readability of Slides
Clarity of Project Objectives and Deliverables
Clicker Scoring
  A - “I get it” - Clear, Nice Job!
  B - “I kind of get it” - Needs More Work
  C - “I’m confused” - Needs Lots of Work

## Slide 26: Who Is Capewell?
“Capewell Aerial Systems is a global leader in aerospace and life support. We are a respected provider of engineered products for aerial delivery, life support and tactical gear for military, law enforcement and humanitarian agencies worldwide. Founded in 1881, Capewell has thrived by helping customers conceive, engineer, prototype, manufacture and field test products that must perform flawlessly in critical situations.”
Back

## Slide 27: Flyback Converter Basics
Uses inductor, capacitor, and switching device (transistor) to change DC voltage levels. Transformer provides electrical isolation.
Back

## Slide 28: Buck Converter Basics
Uses inductor, capacitor, and switching device (transistor) to change DC voltage levels. Output voltage must be lower than input.
Back