## Slide 1: MITRE Technical Presentation Senior Design Project – Solid State Timer Patrick Dunham 2017-11-05

## Slide 3: Presentation Outline
Background
Milestone 1
Milestone 2
Milestone 3
Milestone 4
Conclusions

## Slide 4: Background – Outline
Background
  Sponsor
  Project Statement
  Specifications
Milestone 1
Milestone 2
Milestone 3
Milestone 4
Conclusions

## Slide 5: Background – Sponsor
Supplies products for aerial delivery, life support, and military tactical gear
Owner of multiple smaller companies, including Marktime
Marktime specializes in mechanical timing devices

## Slide 6: Background – Project Statement
Goal:
Design a solid state drop-in replacement for the C10B Electromechanical Cycle Timer. The replacement must meet or exceed the current design in all aspects.
Deliverables:
PCB Design / Schematic
Microcontroller Source Code
Functional Prototype

## Slide 7: Background – Specifications
Power:
Average power draw must be below 3 W.
Each relay must have a maximum rated load of 15 A @ 120 VAC
Timer:
Must control 8 independent devices
Cycle length must be adjustable between 60 – 120 seconds
Must be both factory- and user-programable
Production:
Must cost $40 or less, not including labor
Must match installation footprint of current cycle timer
User Interface:
Must have easily trainable/intuitive interface. Factory interface must allow for lockout of individual device timing changes

## Slide 8: Milestone 1 – Outline
Background
Milestone 1
  Design Approach
  Team Organization
Milestone 2
Milestone 3
Milestone 4
Conclusions

## Slide 9: Milestone 1 – Design Approach
Research Components
TRIACs, SCRs, Relays…
Power Supplies
User Interfaces
Test Circuit
Verify circuit operation
Verify PCB design
Measure component temperatures
Compare to PSPICE model predictions
Design Enclosure
Protect sensitive electronics
Match current enclosure footprint
Manage heat dissipation

## Slide 10: Milestone 1 – Team Organization
5 Components + System Management:
Enclosure - Joshua Reinert [ME]
Relays - Jaileen Algarin [ECE]
Microcontroller - Patrick Dunham [ME / ECE]
Power Supply - Robert Endrizzi [ECE]
User Interface - Nicole Hershman [ECE]
Systems - Patrick Meres [ECE]
Weekly meetings with faculty advisors
Monthly meetings with corporate sponsor
Google Drive for file-sharing/design notebook
Lab Space in ITE C43

## Slide 11: Milestone 2 – Outline
Background
Milestone 1
Milestone 2
  Microcontroller Updates
  Relay Updates
  Power Supply Updates
  User Interface Updates
  Enclosure Updates
Milestone 3
Milestone 4
Conclusions

## Slide 12: Milestone 2 – Microcontroller Operation
Firmware based on 3-state state machine
  Idle State: “Pauses” the cycle, remembering last location
  Cycle State: Runs through the stored cycle, switching on and off relays
  Reset State: Resets the cycle, preparing the device for a new run

## Slide 13: Milestone 2 – Microcontroller Schematic

## Slide 14: Milestone 2 – Microcontroller Schematic
Microcontroller
Relay Control
USB Connector

## Slide 15: Milestone 2 – Relay Schematic

## Slide 16: Milestone 2 – Relay Schematic
Optoisolator
TRIAC
TRIAC Driver

## Slide 17: Milestone 2 – Relay Power Output
RTH(w/o heatsink) : 60 K/W
At 15 A, 15 W of heat is produced (∆T > 900 K!)
Ambient Temp = 60 C
Max Device Temp = 125 C
Need heatsink w/ RTH< 3.13 K/W

## Slide 18: Milestone 2 – Power Supply Solution
Board-mount AC/DC Converter
~$15 Unit Cost
3W output @ 5VDC
Input Voltage: 85 – 264 VAC

## Slide 19: Milestone 2 – UI Hardware
Graphic LCD Screen:
128x64 Display
Size: 2.953 in x 2.075 in x 0.35 in
8-bit parallel interface
-20 to +70 degrees C
Buttons:
PCB-Printed Capacitive Buttons

## Slide 20: Milestone 2 – UI Design

## Slide 21: Milestone 2 – Enclosure
Design must match original enclosure footprint
Does not need to be dustproof/waterproof
Concerns are responsibility of customer
Full enclosure not needed!!!

## Slide 22: Milestone 3 – Outline
Background
Milestone 1
Milestone 2
Milestone 3
  Microcontroller Updates
  Relay Updates
Milestone 4
Conclusions

## Slide 23: Milestone 3 – Microcontroller Board Layout
2.0”
2.0”

## Slide 24: Milestone 3 – Microcontroller Board Layout
Power
USB
Programming
Microcontroller

## Slide 25: Milestone 3 – Relay Schematic

## Slide 26: Milestone 3 – Relay Schematic
Optotriac
TRIAC
Load

## Slide 27: Milestone 3 – Relay Board Layout

## Slide 28: Milestone 3 – Relay Board Layout
Optotriac
TRIAC
Load

## Slide 29: Milestone 3 – Relay Board Layout

## Slide 30: Milestone 4 – Outline
Background
Milestone 1
Milestone 2
Milestone 3
Milestone 4
  PCB Updates
  Microcontroller Updates
  Relay Updates
  User Interface Updates
Conclusions

## Slide 31: Milestone 4 – PCB Revision 1
6.02”
2.82”

## Slide 32: Milestone 4 – PCB Revision 1
Microcontroller
Relays
Power

## Slide 33: Milestone 4 – PCB Revision 2
Timer PCB
LCD PCB

## Slide 34: Milestone 4 – PCB Revision 2
Timer PCB
LCD PCB
Buttons
Relays
Power
LCD
MCU

## Slide 35: Milestone 4 – PCB Issues
Relays not soldered in picture – too close for heatsinks
Original Design
New design – no staggering required!

## Slide 36: Milestone 4 – PCB Issues
Old PSU
New PSU
PCB design doesn’t match footing
Rev. 2 PCB has correct footing
Cheaper custom solution simulations successful
-BUT-
Less expensive module discovered!!!

## Slide 37: Milestone 4 – PCB Issues
PROBLEM: Original mechanical timer receives power ONLY when dishwasher is running
Drop-in replacement design matches that expectation
Illogical to have to run dishwasher to adjust cycle times
SOLUTION: Physical switch added to switch modes
Run Mode – Run dishwasher as normal
Programming Mode – Turn on display, allow user to change programming.

## Slide 38: Milestone 4 – UI Issues
PROBLEM: Current LCD Malfunctioning
LCD will no longer respond to commands
Old, working code no longer works
SOLUTION: Order new LCD, test code
LCD is likely broken. A new module should fix it
Failing this, another screen model is available

## Slide 39: Milestone 4 – Relays

## Slide 40: Conclusions – Outline
Background
Milestone 1
Milestone 2
Milestone 3
Milestone 4
Conclusions
  Estimated Unit Cost
  Final Design Changes
  Future Goals

## Slide 41: Conclusions – Estimated Unit Cost

## Slide 42: Conclusions – Final Design Changes
Smaller Microcontroller Used
256kB memory is significantly larger than needed
Reducing to 32kB does not change code, reduces unit cost by $1
LCD Panel / PCB Not Used
New LCD still did not work with existing code
Components were deemed too expensive for functionality added
Command-line interface over USB used instead

## Slide 43: Conclusions – Future Goals
Replace TRIACS with SMD Variants
Use custom heatsinking solution
Implement smaller, cheaper power supply
Redesign code to allow for PWM control of connected devices

## Slide 44
Questions?